## Slide 1: 可编程逻辑阵列
刘鹏
浙江大学信息与电子工程学院
liupeng@zju.edu.cn
Notes: ROM, SRAM, and PLA

## Slide 2: 可编程逻辑阵列（Programmable Logic Arrays，PLAs)
• • •
inputs
AND array
• • •
outputs
OR array
product terms
Pre-fabricated building block of many AND/OR gates
  Actually NOR or NAND
  ”Personalized" by making or breaking connections among gates
  Programmable array block diagram for sum of products form

## Slide 3: 使能概念（Enabling Concept）
example:
F0 = A + B' C'
F1 = A C' + A B
F2 = B' C' + A B
F3 = B' C + A
personality matrix
1 = uncomplemented in term
0 = complemented in term
– = does not participate
1 = term connected to output
0 = no connection to output
input side:
output side:
product inputs outputs
term A B C F0 F1 F2 F3 AB 1 1 – 0 1 1 0 B'C – 0 1 0 0 0 1 AC' 1 – 0 0 1 0 0 B'C' – 0 0 1 0 1 0 A 1 – – 1 0 0 1
reuse of terms
Shared product terms among outputs

## Slide 4: 编程前
All possible connections available before "programming"
  In reality, all AND and OR gates are NANDs

## Slide 5: PLD符号

## Slide 6: 编程后
A
B
C
F1
F2
F3
F0
AB
B'C
AC'
B'C'
A
Unwanted connections are "blown"
  Fuse (normally connected, break unwanted ones)
  Anti-fuse (normally disconnected, make wanted connections)

## Slide 7: 高扇入（Fan-in）结构的一种表示
notation for implementing
F0 = A B + A' B'
F1 = C D' + C' D
AB+A'B'
CD'+C'D
AB
A'B'
CD'
C'D
A
B
C
D
Short-hand notation--don't have to draw all the wires
  Signifies a connection is present and perpendicular signal is an input to gate

## Slide 8: 可编程逻辑阵列例子
A B C F1 F2 F3 F4 F5 F6
0 0 0 0 0 1 1 0 0
0 0 1 0 1 0 1 1 1
0 1 0 0 1 0 1 1 1
0 1 1 0 1 0 1 0 0
1 0 0 0 1 0 1 1 1
1 0 1 0 1 0 1 0 0
1 1 0 0 1 0 1 0 0
1 1 1 1 1 0 0 1 1
A'B'C'
A'B'C
A'BC'
A'BC
AB'C'
AB'C
ABC'
ABC
A
B
C
F1
F2
F3
F4
F5
F6
full decoder as for memory address
bits stored in memory
Multiple functions of A, B, C
  F1 = A B C
  F2 = A + B + C
  F3 = A' B' C'
  F4 = A' + B' + C'
  F5 = A xor B xor C
  F6 = (A xnor B xnor C)’

## Slide 9: PLA 设计例子
0 1 X 0
0 1 X 0 0 0 X X
0 0 X X
D
A
B
C
minimized functions:
W = A + B D + B C
X = B C'
Y = B + C
Z = A'B'C'D + B C D + A D' + B' C D'
A B C D W X Y Z 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 1 0 0 1 0 0 0 1 1 0 0 1 1 0 0 1 0 0 1 0 0 0 1 1 0 0 1 0 1 1 1 1 0 0 1 1 0 1 0 1 0 0 1 1 1 1 0 1 1 1 0 0 0 1 0 0 1 1 0 0 1 1 0 0 0 1 0 1 – – – – – 1 1 – – – – – –
0 0 X 1
0 1 X 1 0 1 X X
0 1 X X
D
A
B
C
K-map for W
K-map for X
0 1 X 0
0 1 X 0 1 1 X X
1 1 X X
D
A
B
C
K-map for Y
BCD to Gray code converter
K-map for Z
0 0 X 1
1 0 X 0 0 1 X X
1 0 X X
D
A
B
C

## Slide 10: PLA 设计例子
not a particularly good
candidate for PLA
implementation since no terms are shared among outputs
however, much more compact and regular implementation when compared with discrete AND and OR gates
A B C D
W X Y Z
A
BD
BC
BC'
B
C
A'B'C'D
BCD
AD'
BCD'
minimized functions:
W = A + B D + B C
X = B C'
Y = B + C
Z = A'B'C'D + B C D + A D' + B' C D'
Code converter: programmed PLA

## Slide 11: PLA设计例子
0 1 X 0
0 1 X 0 0 0 X X
0 0 X X
D
A
B
C
minimized functions:
W =
X =
Y =
Z =
A B C D W X Y Z 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 1 0 0 1 0 0 0 1 1 0 0 1 1 0 0 1 0 0 1 0 0 0 1 1 0 0 1 0 1 1 1 1 0 0 1 1 0 1 0 1 0 0 1 1 1 1 0 1 1 1 0 0 0 1 0 0 1 1 0 0 1 1 0 0 0 1 0 1 – – – – – 1 1 – – – – – –
0 0 X 1
0 1 X 1 0 1 X X
0 1 X X
D
A
B
C
K-map for W
K-map for X
0 1 X 0
0 1 X 0 1 1 X X
1 1 X X
D
A
B
C
K-map for Y
BCD to Gray code converter
K-map for Z
0 0 X 1
1 0 X 0 0 1 X X
1 0 X X
D
A
B
C

## Slide 12: PLA 设计例子#1
0 1 X 0
0 1 X 0 0 0 X X
0 0 X X
D
A
B
C
minimized functions:
W =
X =
Y =
Z =
A B C D W X Y Z 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 1 0 0 1 0 0 0 1 1 0 0 1 1 0 0 1 0 0 1 0 0 0 1 1 0 0 1 0 1 1 1 1 0 0 1 1 0 1 0 1 0 0 1 1 1 1 0 1 1 1 0 0 0 1 0 0 1 1 0 0 1 1 0 0 0 1 0 1 – – – – – 1 1 – – – – – –
0 0 X 1
0 1 X 1 0 1 X X
0 1 X X
D
A
B
C
K-map for W
K-map for X
0 1 X 0
0 1 X 0 1 1 X X
1 1 X X
D
A
B
C
K-map for Y
BCD to Gray code converter
K-map for Z
0 0 X 1
1 0 X 0 0 1 X X
1 0 X X
D
A
B
C
BC’

## Slide 13: PLA 设计例子#2
EQ NE LT GT
A'B'C'D'
A'BC'D
ABCD
AB'CD'
AC'
A'C
B'D
BD'
A'B'D
B'CD
ABC
BC'D'
A B C D
Magnitude comparator
1 0 0 0
0 1 0 0 0 0 1 0
0 0 0 1
D
A
B
C
0 1 1 1
1 0 1 1 1 1 0 1
1 1 1 0
D
A
B
C
0 0 0 0
1 0 0 0 1 1 0 1
1 1 0 0
D
A
B
C
0 1 1 1
0 0 1 1 0 0 0 0
0 0 1 0
D
A
B
C
K-map for EQ
K-map for NE
K-map for GT
K-map for LT

## Slide 14: 多路选择器/解复器
multiplexer
demultiplexer
4x4 switch
control
control
Direct point-to-point connections between gates
Multiplexer: route one of many inputs to a single output
Demultiplexer: route single input to one of many outputs

## Slide 15: 多路选择器
two alternative forms
for a 2:1 Mux truth table
functional form
logical form
A Z 0 I0 1 I1
I1 I0 A Z 0 0 0 0 0 0 1 0 0 1 0 1 0 1 1 0 1 0 0 0 1 0 1 1 1 1 0 1 1 1 1 1
Z = A' I0 + A I1
Multiplexers/Selectors: general concept
  2n data inputs, n control inputs (called "selects"), 1 output
  Used to connect 2n points to a single point
  Control signal pattern forms binary index of input connected to output

## Slide 16: 多路选择器
2:1 mux: Z = A' I0 + A I1
4:1 mux: Z = A' B' I0 + A' B I1 + A B' I2 + A B I3
8:1 mux: Z = A'B'C'I0 + A'B'CI1 + A'BC'I2 + A'BCI3 + AB'C'I4 + AB'CI5 + ABC'I6 + ABCI7
In general, Z =  (mkIk)
  in minterm shorthand form for a 2n:1 Mux
2 -1
I0 I1 I2 I3 I4 I5 I6 I7
A B C
8:1 mux
Z
I0 I1 I2 I3
A B
4:1 mux
Z
I0 I1
A
2:1 mux
Z
k=0
n

## Slide 17: 多路选择器级联
control signals B and C simultaneously choose one of I0, I1, I2, I3 and one of I4, I5, I6, I7 control signal A chooses which of the upper or lower mux's output to gate to Z
alternative implementation
C
Z
A B
4:1 mux
2:1 mux
2:1 mux
2:1 mux
2:1 mux
I4 I5
I2 I3
I0 I1
I6 I7
8:1 mux
Large multiplexers implemented by cascading smaller ones
Z
I0 I1 I2 I3
A
I4 I5 I6 I7
B C
4:1 mux
4:1 mux
2:1 mux
8:1 mux

## Slide 18: 多路选择器作为查找表（Lookup Tables，LUTs）
C
A
B
0 1 2 3 4 5 6 7
1 0 1 0 0 0 1 1
S2
8:1 MUX
S1
S0
F
2n:1 multiplexer implements any function of n variables
  With the variables used as control inputs and
  Data inputs tied to 0 or 1
  In essence, a lookup table
Example:
  F(A,B,C) = m0 + m2 + m6 + m7 = A'B'C' + A'BC' + ABC' + ABC = A'B'(C') + A'B(C') + AB'(0) + AB(1)

## Slide 19: 多路选择器作为查找表（Lookup Tables，LUTs）
A B C F 0 0 0 1 0 0 1 0 0 1 0 1 0 1 1 0 1 0 0 0 1 0 1 0 1 1 0 1 1 1 1 1
C' C' 0 1
A
B
S1
S0
F
0 1 2 3
4:1 MUX
C' C' 0 1
F
C
A
B
0 1 2 3 4 5 6 7
1 0 1 0 0 0 1 1
S2
8:1 MUX
S1
S0
2n-1:1 mux can implement any function of n variables
  With n-1 variables used as control inputs and
  Data inputs tied to the last variable or its complement
Example:
  F(A,B,C) = m0 + m2 + m6 + m7 = A'B'C' + A'BC' + ABC' + ABC = A'B'(C') + A'B(C') + AB'(0) + AB(1)

## Slide 20: 多路选择器作为查找表（Lookup Tables，LUTs）
Generalization
Example: F(A,B,C,D) implemented by an 8:1 MUX
n-1 mux control variables
  single mux data variable
four possible
configurations of truth table rows
can be expressed as a function of In
choose A,B,C as control variables multiplexer implementation
I0 I1 . . . In-1 In F . . . . 0 0 0 1 1 . . . . 1 0 1 0 1 0 In In' 1
C
A
B
0 1 2 3 4 5 6 7
1 D 0 1 D’ D D’ D’
S2
8:1 MUX
S1
S0
1 0
1 0
1 1
0 0
D
A
1 1
0 1
0 1
1 0
B
C

## Slide 21: 解复器 / 译码器
1:2 Decoder:
O0 = G  S’
O1 = G  S
2:4 Decoder:
O0 = G  S1’  S0’
O1 = G  S1’  S0
O2 = G  S1  S0’
O3 = G  S1  S0
3:8 Decoder:
O0 = G  S2’  S1’  S0’
O1 = G  S2’  S1’  S0
O2 = G  S2’  S1  S0’
O3 = G  S2’  S1  S0
O4 = G  S2  S1’  S0’
O5 = G  S2  S1’  S0
O6 = G  S2  S1  S0’
O7 = G  S2  S1  S0
Decoders / demultiplexers: general concept
  Single data input, n control inputs, 2n outputs
  Control inputs (called “selects” (S)) represent binary index of output to which the input is connected
  Data input usually called “enable” (G)

## Slide 22: 解复器作为通用逻辑
demultiplexer generates appropriate
Min-term based on control signals
(it "decodes" control signals)
n:2n decoder implements any function of n variables
  With the variables used as control inputs
  Enable inputs tied to 1 and
  Appropriate min-terms summed to form the function
A'B'C' A'B'C A'BC' A'BC AB'C' AB'C ABC' ABC
C
A
B
0 1 2 3 4 5 6 7
S2
3:8 DEC
S1
S0
“1”

## Slide 23: 解复器作为通用逻辑
F1
F2
F3
F1 = A' B C' D + A' B' C D + A B C D
F2 = A B C' D’ + A B C
F3 = (A' + B' + C' + D')
A
B
0 A'B'C'D' 1 A'B'C'D 2 A'B'CD' 3 A'B'CD 4 A'BC'D' 5 A'BC'D 6 A'BCD' 7 A'BCD 8 AB'C'D' 9 AB'C'D 10 AB'CD' 11 AB'CD 12 ABC'D' 13 ABC'D 14 ABCD' 15 ABCD
4:16 DEC
Enable
C
D

## Slide 24: 译码器级联
0 A'B'C'D'E' 1 2 3 4 5 6 7
S2
3:8 DEC
S1
S0
A
B
0 1 2 3
S1
2:4 DEC
S0
F
0 1 2 A'BC'DE' 3 4 5 6 7
S2
3:8 DEC
S1
S0
E
C
D
0 AB'C'D'E' 1 2 3 4 5 6 7 AB'CDE
5:32 decoder
  1x2:4 decoder
  4x3:8 decoders
3:8 DEC
0 1 2 3 4 5 6 7 ABCDE
E
C
D
S2
S1
S0
S2
3:8 DEC
S1
S0

## Slide 25: 只读存储器（ROM）
decoder
0 n-1
  Address
2 -1
n
0
1
1
1
1
word[i] = 0011 word[j] = 1010
bit lines (normally pulled to 1 through resistor – selectively connected to 0 by word line controlled switches)
j
i
internal organization
word lines (only one is active – decoder is just right for this)
Two dimensional array of 1s and 0s
  Entry (row) is called a "word"
  Width of row = word-size
  Index is called an "address"
  Address is input
  Selected word is output

## Slide 26: ROM和组合逻辑
F0 = A' B' C + A B' C' + A B' C
F1 = A' B' C + A' B C' + A B C
F2 = A' B' C' + A' B' C + A B' C'
F3 = A' B C + A B' C' + A B C'
truth table
A B C F0 F1 F2 F3
0 0 0 0 0 1 0 0 0 1 1 1 1 0 0 1 0 0 1 0 0 0 1 1 0 0 0 1
1 0 0 1 0 1 1
1 0 1 1 0 0 0
1 1 0 0 0 0 1
1 1 1 0 1 0 0
block diagram
ROM 8 words x 4 bits/word
address
outputs
A B C F0 F1 F2 F3
Combinational logic implementation (two-level canonical form) using a ROM

## Slide 27: ROM结构
Similar to a PLA structure but with a fully decoded AND array
  Completely flexible OR array (unlike PAL)
n address lines
• • •
inputs
decoder
2n word lines
• • •
outputs
memory array (2n words by m bits)
m data lines

## Slide 28: ROM与 PLA对比
ROM
  Design time is short (no need to minimize output functions)
  Most input combinations are needed (e.g., code converters)
  Little sharing of product terms among output functions
  Size doubles for each additional input
  Can't exploit don't cares
  Cheap (high-volume component)
  Can implement any function of n inputs
  Medium speed
PLA
  Design tools are available for multi-output minimization
  There are relatively few unique min-term combinations
  Many min-terms are shared among the output functions
  Most complex in design, need more sophisticated tools
  Can implement any function up to a product term limit
  Slow (two programmable planes)

## Slide 29: 扩展字大小和存储容量

## Slide 30: 地址译码的系统例子
Notes: In many instances, it is necessary to use various memory devices in the same memory system.
The ROM portion is made up of two 8K x 8 devices (PROM-0 and PROM-1).
The RAM section requires a single 8K x 8 device.
The EEPROM available is only a 2K x 8 device.
The memory system requires a decoder to select only one device at a time. This decoder divides the entire memory space (assuming 16 address bits) into 8K address blocks.
The upper three address lines control the decoder.
The 13 lower-order address lines are tied directly to the address inputs on the memory chips.
The only exception to this the EEPROM, which has only 11 address lines for its 2-Kbyte capacity.
The same contents of the EEPROM will also appear at the addresses 6800-6FFF, 7000-77FF, and 7800-7FFF.